## Slide 1
Field | Central Heating
Chapter | Fuel Storage
Subtitle | Fuel Oil Tanks

## Slide 2: Fuel Oil Tanks

## Slide 3: Manner of storage
1. not accessible fuel oil tanks
2. accessible fuel oil tanks

## Slide 4: not accessible fuel oil tanks
Reservoir in filled up pit

## Slide 5: not accessible fuel oil tanks
Reservoir directly buried

## Slide 6: accessible fuel oil tanks
Reservoir in open air

## Slide 7: accessible fuel oil tanks
Reservoir in accessible pit

## Slide 8: Materials for construction
Steel reservoir with 2 layers of anti-rust paint ( accesseble )
Steel reservoir with a epoxy coating or polyurethane coating ( unaccessable )
PE reservoir ( accessseble )
PE reservoir with reinforcing ribs ( unaccessable )
Stainless steel reservoir ( very expensive )
All reservoirs have to be double-walled

## Slide 9: Identification plate
Name and address of the constructor
Date and manufacturingnumber
Reference of the prototype inspection
EN norm of the reservoir
Volume and dimensions of the reservoir
Proof in bar

## Slide 10: Principle diagram of storage in a double-walled tank