## Slide 1
Field | Central Heating
Chapter | Regulations concerning the annual maintenance of installations
Subtitle | The Exhaust Duct Type C Appliances

## Slide 2
The Exhaust Duct of the Combustion Products for Type C Appliances
The combustion air supply duct, the combustion products exhaust duct, the appliance connections to these ducts and the end piece of type C appliances
Must be made with materials prescribed by the manufacturer and installed according to the technical installation instructions, which are part of the CE approval.

## Slide 3
The Exhaust Duct of the Combustion Products for Type C Appliances
Ensure sufficient free space around the terminal wall penetration for free dispersion of combustion products. Minimum distances from the outlet to access or ventilation openings should be based on the dilution factor of the emitted products.

## Slide 4
Fire Safety
The plastic exhaust duct of a gas boiler with a closed combustion circuit can be fitted within a metal duct and placed in a pipe, if the boiler's combustion air supply occurs through the space between the exhaust duct and the metal pipe.
If the outer duct of the concentric ducts of the supply and exhaust system for C boilers is made of metal, no special requirements are imposed on the ventilation of the spaces through which these ducts run.