## Slide 1
Field | Central Heating
Chapter | Heating Theory & Heating Techniques
Subtitle | Heating appliances

## Slide 2: HEATING APPLIANCES
Heating appliances are devices designed to provide warmth and increase the temperature of a space. They can be used for residential, commercial, and industrial purposes.

## Slide 3
Here are some of the main gas furnace components to know.
Thermostat: A temperature activated switch that signals to the furnace, via a control board, that the home needs heat (indoor temperature dips below a set point). This signal turns on ithe ignition switch in the furnace to light the burners.
Draft Hood/Fan: The fan draws air into the burner assembly where it mixes with gas to create combustion.
Burners: Like a gas grill, furnace burners are a set of tubes through which gas is directed and burned
Heat exchanger: A series of metal tubes that are heated by the burners in order to warm the inside air
Blower: The blower fan directs air coming from return ducts into the hot heat exchanger.
Flue: The flue vent collects the spent combustion gases used to create heat and carries them outside the home.

## Slide 4: RADIATOR
Radiators work by utilizing convection and radiation to transfer heat from a hot surface to the surrounding air. They are commonly used in heating systems to warm up indoor spaces.
Heating Source: Radiators are connected to a heating system, such as a boiler or a heat pump, which produces hot water or steam.
Heat Transfer: The hot water or steam enters the radiator through an inlet valve and flows through a series of pipes or fins within the radiator.
Convection: As the hot water or steam passes through the pipes or fins, it transfers heat to the metal surface of the radiator.
Radiation: The hot metal surface of the radiator emits infrared radiation, which can directly heat objects and people in the room. This radiation contributes to warming the space.
Heat Distribution: The heated air and radiation from the radiator warm up the surrounding room.
Thermostat Control: The heating system is usually equipped with a thermostat that senses the room temperature.

## Slide 5: BASEBOARD HEATER
Baseboard heaters are electric heaters installed along the baseboards of a room. They work by convection, where the cool air enters the heater at the bottom, gets heated, and rises, creating a circulation of warm air.

## Slide 6: HEAT PUMPS
The heat pump itself consists of a compressor, which moves a refrigerant through a refrigeration cycle, and a heat exchanger, which extracts heat from the source.

## Slide 7: ELECTRIC FIREPLACE
Electric fireplaces provide the visual ambiance of a traditional fireplace while also producing heat. They use electricity to power heating elements and often have built-in fans to distribute warm air.

## Slide 8: INFRARED HEATER
Infrared heaters emit infrared radiation that directly heats objects and people in its path. They are often used for outdoor spaces, patios, or garages.

## Slide 9: CENTRAL HEATING SYSTEM
This type of heating system is commonly used in larger buildings or homes. It consists of a central heating unit, such as a boiler or furnace, which heats water or air. The heated water or air is then distributed throughout the building via ducts, pipes, or radiators.

## Slide 10: References
Daken, A. (n.d.). How Does a Heat Pump Work? Retrieved from Energy Star: https://www.energystar.gov/products/ask-the-experts/how-does-heat-pump-work
What Are the Main Parts of a Furnace? (2022 , September 28). Retrieved from Herchenbach Mechanical Heating and Cooling: https://www.herchenbach.com/blog/what-are-the-main-parts-of-a-furnace
Deziel, C. ( 2024, Febuary 06). Understanding the Different Parts of a Furnace. Retrieved from Family Handiman: https://www.familyhandyman.com/article/parts-of-a-furnace/
Active Indirect Water Heater Diagram.svg. (2010, April 18). Retrieved from Wikimedia Commons: https://commons.wikimedia.org/wiki/File:Active_Indirect_Water_Heater_Diagram.svg
What is Central Heating? Different Central Heating Systems UK Guide. (2024, May 21st). Retrieved from iheat: https://iheat.co.uk/boiler-help/different-types-of-central-heating-systems Central heating. (2024, May 27). Retrieved from Wikipedia: https://en.wikipedia.org/wiki/Central_heating
How does a radiator central heating work? (2016 , May 9). Retrieved from Central Heating: https://www.central-heating.co.nz/how-does-a-radiator-central-heating-work/
Radiator. (2024, April 21). Retrieved from Wikipedia: https://en.wikipedia.org/wiki/Radiator
Dunn, D. S. (2024, May 31). How Do Radiator Heaters Work? Retrieved from Today's Homeowner: https://todayshomeowner.com/hvac/guides/how-do-radiator-heaters-work/
HEAT PUMP / part 1 - principle of operation and structure. (2023, July 15). Retrieved from hajster: https://hajster.com/en/heat-pump-part-1-principle-of-operation-and-structure-en
Infrared heater. (2024, May 13). Retrieved from Wikipedia: https://en.wikipedia.org/wiki/Infrared_heater