## Slide 1: Plastic Pipes
Field | Central Heating
Chapter | Materials and installation technology for central heating
Subtitle | Plastic pipes

## Slide 2: Types of Plastic
Thermoplastics
Thermosets
Elastomers

## Slide 3: PVC : applications
Wastewater
Water drainage : rain
Compressed air
Swimming pool pipes

## Slide 4: PVC : diameters
32 mm
40 mm
50 mm
75 mm
90 mm
110 mm
125 mm

## Slide 5: PVC : connection techniques
Fittings with seal
Fittings for gluing

## Slide 6: PE : types of PE
LDPE : low density PE
HDPE : high density PE
XPE : reticulated PE

## Slide 7: HDPE : applications
Wastewater
Water drainage : rain
Distribution of drinking water
Distribution of gas

## Slide 8: HDPE : diameters
32 mm
40 mm
50 mm
70 mm
80 mm
100 mm

## Slide 9: HDPE : connection techniques
Mirror welding

## Slide 10: HDPE : connection techniques
Socket welding

## Slide 11: HDPE : connection techniques
Electro fusion pipe welding

## Slide 12: XPE : applications
Distribution cold drinking water
Distribution warm drinking water

## Slide 13: XPE : diameters
16 mm
20 mm
25 mm
32 mm

## Slide 14: PP ( polypropeen ) : applications
Distribution cold drinking water
Compressed Air

## Slide 15: PP : diameters
16 mm
20 mm
25 mm
32 mm
40 mm
50 mm

## Slide 16: PP : connection techniques
Welding PP

## Slide 17: Multilayer pipe

## Slide 18: Multilayer pipe : applications
Distribution of cold drinkingwater
Distribution of warm drinkingwater
Central heating tubes

## Slide 19: Multilayer pipe : diameters
12 mm
16 mm
20 mm
26 mm
32 mm

## Slide 20: Multilayer pipe : connection techniques
Mechanical connection

## Slide 21: Multilayer pipe : connection techniques
Press connection