Foundations

---
Field	Construction
Chapter	Foundations
Subtitle	Foundationplan

---
What should we add on a foundationplan ?

---
Length and width of foundation
Depth of foundation
Ordinary foundation or shallow foundation or strip foundation
Is there a fork beach provided ?
Drainage pipes for toilets, washing machines, bathrooms and dishwater
Rainwater drainage and dry weather drainage
Connection of utilities (water, gas, internet,electricity)

---
Linetypes on a foundation plan

---
Linetype	Purpose
Full black line	Foundation soles
Black dashed line	Higer level
Blue dashed line	Drainage pipes rainwater
Red dashed line	Drainage pipes dirty water

---
Field	Construction
Chapter	Foundations
Subtitle	Purpose of a foundation and Foundation types

---
Purpose of a foundation
Distribute and transfer the load of a building on a ground with a high load bearing capacity.
The foundation cannot prevent the building from deforming , but must ensure even subsidence to prevent cracking.

---
Foundation types
Choice of type of calculation: according to a calculation of an engineer.
After:
-soil study
-soil test

---
Type 1
Ordinary foundation (shallow foundation)
Is a construction of concrete strips where the walls have to come. The width of these strips must be in proportion to the load that the walls will carry.
The outer walls must be able to support on wider concrete strips than the interior walls.

---
Type 2
Foundation soles
features
Ever wider than the masonry
The large width of the foundation soles gives a larger surface area and a better distribution of the load.
conditions for the load
Load: preferably centric
Pillar (usually square): must be placed in the middle (pillars in reinforced concrete)
The reinforced concrete distributes the load evenly, so the pillar cannot be pushed through the foundation.

---
Type 3
Strip foundation:
The difference with a shallow foundation is that reinforced concrete is used
Concrete strips are laid on +/- 80 cm below ground level

---
Ground level ?
The ground level is the top of the ground of the ground . For buildings , this is usually about 15 cm below the top of the finished floor

---
Type 4
General foundation plate or floating floor plate :
The ground’s carrying force must be the same throughout the surface
Create a fork on approximately 80 cm deep at exterior walls

---
A general foundation plate is chosen for building sites where the carrying capacity is not sufficient for a direct foundation on steel

---
Important :
Make sure that all the facilities are taken as regards e.g. the toilet , washing machine , dishwasher etc…. , to ensure the drainage .
Don’t forget to install the utility junction

---
What are utilities?
In our modern society , utilities are of unprecedented importance.
Utilities are available for gas , electricity , distribution , internet & water

---
An energy curve has 5 connections :
2x diameter 110mm : gas & water
1x diameter 75mm : electricity
2x diameter 50mm: telephony/internet
Where are the energy throughputs located?
Via a connection in the basement , garage or storage room

---
Type 5
Pole –foundation :
Has been designated for parcels whose soil only has sufficient capacity at great depth
This method is often used when foundation is to be built at a depth of 5m below the ground

---
The pole foundation is a construction of concrete or wooden poles that can be placed in the ground at points where the building will exert a great pressure
On top of these poles, a grid of beams ends up in reinforced concrete

---
Methods :
Normal pole foundation:The poles are driven into the ground using a pile driving machine
Screwed poles :
Be fitted with a drill , which has a thread and a cone on the head which displaces the ground against the wall of the pre-made hole

---
When the pole is at the correct depth, the drill is retracted, concrete is pressed into the hole trough the hollow core of the drill, creating the pole
Additional reinforcement is triked into the immediately after pressing the concrete

---
Type 6
Pits foundation :
Is used when the medium depth of the resilient soil is between 4 en 8 m deep
The foundation consist of a number of pillars that are formed in the ground and reach to or in the resilient layer

---
A pillar consist of a number of concretes placed on top of each other, which sink into the ground by their own weight when the ground is dug away within the rings
The lower ring has a cutting edge

---
If a ring is almost sunk in the bottom, a further one is placed on top. This process is repeated until the high-capacity layer is reached .
The filling consist of unreinforced concrete.
The concrete rings have a diameter of 1 to 3m

---
On the so-called pillars are the foundation beams that carry the building
Normal pit foundation and pit foundation with round grapple bucket

---
Ground loop

---
Ground loop :
Why?
It is an essential part of a safe electrical installation with the main goal of preventing electrocution .

---
The grounding of your house is mandatory in Belgium and is included in the general regulations on the electrical installations , in short the AREI

---
Material for the ground loop?
A copper white conductor with a section of min. 35mm² or a free copper conductor where the copper has a section of 10mm² and the entire conductor has a section of 35mm²

---
Length :
Depending on the outside circumference of the house
Measure the perimeter of the house and add 4 m extra depending on the depth of the foundation or basement for the cable to be raised

---
Important , placement :
Provide a conductor and 2 pieces of flexible pvc protective tubes of about 3 meters , and possibly a metal clip .

---
Order of placement:
Make a 5 to 10cm slot deep in the outer foundation slots or under the basement plate
Start now at the place where the elctricity cabinet is provided . Stay about 1m above the zero level

---
*Place the conductor in the slot and follow the outside edge of the building until you reach the electrical cabinet .
*Then you go up again with the guide, also 1m above the zero level

---
*Now slide the pvc protective tubes about 50 cm above the zero level on the both ends of the guide . The protection should be slightly inserted into the slot .
Now cover the 5 to 10cm slot with sand ,make sure that the guide is not visible anywhere

---
The conductor must never come into contact with the foundation , even with concrete & mortar.
Attach the 2 ends to the metal clip that can be secured against the wall at the finish

---
The loop must be made from one piece , connections under the foundation are forbidden .
Exceptions are discussed first with the architect .
If there any signs of blisters , the connections must be visible

---
Ground loop and clamps

---
Calculation of the amount of concrete

---
Calculation of amount of concrete for foundations.
Multiply:
*The length of the outer wall
*The depth of the outer foundation wall
*The height of the foundation
Do this also for the inner foundation wall and make the difference from both results

---
Multiply the necessary volume by the number of kilograms of ingredients, taking into account that for the approx .1m³ concrete with a strength of 250 kg /m³ (specie with a ratio of 1:2:3 )
you need the following
*Portlandcement CEMI and klasse 32.5:ca.250kg
*Rhine sand : 0/2 , ca. 750kg
*Gravel, grain size 4/14, approx. 1000kg

---
Example using a building plan :
Length of the outer foundation wall = L(a)=1,69m
Inner foundation wall length = L(b)= 1,09m
Depth of outer foundation wall=d(a)=1,69m
Depth of inner foundation wall =d(b)=1,09m
Heigth of foundation =h=0.60m

---
(L(a)xd(a)xh)-L(b)xd(b)xh)= volume foundation slots = amount of concrete
Calcultion:
(1.69mx1.69mx0.60m) –(1.09mx1.09mx0.60m)=1.71m-0.71m=1m³
Portlandcement CEMI and class 32.5 ca. 250kgx1m³= 250kg

---
Rhinesand 0/2, ca.750 kgx1m³=750kg
Gravel : grain size 4/14 ca.1000kg x1m³= 1000kg .

---
Floor plate :
In order to know the amount of concrete: First calculate the volume of that floor plate Multiply:
1 : The lenght of the floor plate
2: The width of the floor plate
3 : The height ( thickness) of the floor plate

---
Multiply the necessary volume by the number of kilograms of components , knowing that for approx . 1m³ concrete with a ratio of 1:2:3 you need the following :
*Portlandcement CEMI and class 32,5 ca. 350kg
Rhinesand 0/2 : ca. 700kg
Gravel: grain size 4/14 : ca. 1050kg

---
Example of a construction plan :
Length floor plate : L = 1.40m
Width floor plate : b = 1.40m
Height floor plate : h = 0.12m

---
L x b x h = Volume floor plate = amount of concrete
1.40 m x 1.40 m X 0.12m = 0.24 m³
Portlandcement CEMI and class 32,5 ca. 350kg x 0.24m³ = 84kg
Rijnsand 0/2 : ca. 700kg x 0.24= 168kg
Gravel : grain size 4/14 , ca.1050kg x0.24m³= 252kg