## Slide 3
Load-bearing interior
walls:
What is a load-bearing inner wall?
It carries the weight of the
overhead structure (the weight of the floor or roof structure above).

## Slide 4
Transfers the forces to the
foundation.
Never remove these walls during
renovations.
If you do so, the load-bearing function must be replaced.

## Slide 5
Replace it by another construction element for example: a beam.
Replacing it with a steel beam is
also possible.

## Slide 6
How many load-bearing interior
walls are there?
There are at least 4 load-bearing walls.
With a long span you have more chance of load-bearing interior walls.
Load-bearing interior walls close
off any space.

## Slide 7
Walls on wich floors and beams
lean= load-bearing wall.
Thickness of a load-bearing wall.
It must be more than 10cm
The most common thicknesses are 14 cm and 19 cm.

## Slide 8
Examples :

## Slide 9: Non load-bearing interior walls:

## Slide 10
Recognizable by their smaller thickness ( 9 cm).
They are not supporting other building
elements.
It serves as a room layout.
Recommended for a partition wall=
7-10cm thick.

## Slide 11
Wall openings in non-load-
bearings walls are bridged by:
Concrete, steel or wooden lintels.
Non-load-bearing walls are usually glued.

## Slide 12
Materials:
Plaster, aerated concrete,
concrete, quick-build blocks.
a)Gypsum blocks:
Non-insulating, moisture resistant
Hydro gypsum blocks for bathroom and kitchen.

## Slide 13
Process:
Tongue and groove system.
Glued with glue based on plaster.
Filming the connection joints and
joints with plaster glue.
Direct wallpapering and painting
can be done.

## Slide 14
b)Aerated concrete:
Low density concrete.
Strong insulating capacity.
Fire resistant.
Heat-accumulating capacity.
Frost resistant.

## Slide 15
Process:
It is usually glued.
The surface must be clean.
If there is an uneven surface= 1st layer has to go off.
The horizontal bricklaying with mortar. Further apply glue, place subsequent layers.

## Slide 16
Anchoring other walls is necessary.
Anchoring with galvanized spring
anchor.
Securing spring anchor with impact
sleeve or wire nail.

## Slide 17
c) Concrete, solid wall:
Is usually a prefabricated wall.
In reinforced concrete.
Walls are made with a 10cm
thickness.

## Slide 18
Airtightness of the walls is
important.
Air leaks significantly reduce
sound isolation.
@Megaton/Structo prefab Systems.

## Slide 19
d) Quick building blocks:
Still the most used blocks.
They are perforated bricks of a larger size.
They are lighter and easy to use.
They are actually only suitable for non-visible masonry.

## Slide 20
Exceptions: garages.
Joints are added immediatly.
The most commonly used quick-
build block for interior walls is:
290x140x90mm
But they also use 290x 140x 140mm

## Slide 21
Anchor these in the inner
walls of the cavity wall.
The interior walls are connected
with each other.
Quick building blocks 290x90x140
L x BR x H

## Slide 22
Quick building blocks
290 x 140 x 140
L X BR x H