## Slide 3
Outer cavity wall
Facades:
Normally a building consists of 4
facades.
1: Front facade – 2: Back facades
3 and4: right- and left side facade.

## Slide 4
The front facade is also the
building line.
Function of the facades:
Protection against wind, moisture
and drafts.

## Slide 5
Aesthetic function
Determined by several elements.
1: The materials used.
2: The type of grouting.
3: The details that can be found.

## Slide 6
Materials:
1:Facing bricks
We already discussed these in a
previous chapter.
On the next page you can find different images of facing bricks.

## Slide 7
Images of facing bricks:
Hand-moulded stones
@wienerberger
Strict press stone Molded brick

## Slide 8
Clickbrick @wienerberger

## Slide 9
2: Stone strips:
They are real stones, thinly sawn.
No visible difference with real stones
They are glued to an existing wall.
(usually against insulation boards).
As an alternative to crepi ( a coat of plaster).

## Slide 10
Advantages of stone strips:
1: Space-saving
2: Authentic view of stone.
3:Quick installation.
There are also stone strips made
of ceramic tiles and in natural
stone.

## Slide 11
Placement stone strips:
1: On insulation:
By bonding
With or without grout.
2:On a dry, flat, dust- and grease free surface.

## Slide 12
Images stone strips:
Stone strips Natural stone
@livios strips
@façade works

## Slide 13
Facade plastering:
Can be used on both old and new
exterior facades.
The most famous is crepi (a coat of plaster).
It is a good combination with
insulation.

## Slide 14
There are 2 types of crepi (coat of plaster):
1: One with synthetic resin.
This a flexible product
The chances of laceration or damage are
small.
The wall is protected against moisture and frost.

## Slide 15
It is also excellent to combine with
insulation.
Good attachment to all surfaces.

## Slide 16
2:Crepi (coat of plaster) based on minerals:
It’s a natural mixture of sand, lime and
cement.
The best option for decorative
finishing.
You can apply relief or texture
with this one.

## Slide 17
It also offers weather protection.
It is a bit more stiff than synthetic resin
It is best applied in a quiet
environment.

## Slide 18
Advantages and
disadvantages of crepi (a coat of plaster)
1:Advantages:
Protection against moisture.
Energy-saving and many colors.
Fits all homes.

## Slide 19
2: Disadvantages:
Difficult to clean.
The color can change.
Crepi.be Pinterest Crepi.be
White crepy Black crepy

## Slide 20
Spray cork
What is spray cork?
Facade cladding made of cork
granules or cork granulates.
With acrylic resin and vegetal oils.
Sometimes there is an addition of pigments.

## Slide 21
It gives gives either a rough or a
smooth finish.
Rough finish= rural appearance.
Smooth finish= modern homes.

## Slide 22
Advantages-disadvantages.
1:Advantages:
An environmentally friendly way of facade cladding.
Easy to apply.
It can be applied to all types of
surfaces.

## Slide 23
Spray cork also has an insulating
effect, thermally and
acoustically.
The insulating effect helps replace
cold bridges.
It also has a moisture-resistant effect.
Many decorative possibilities.

## Slide 24
Spray cork is elastic.
It has an high resistance to laceration and damage.
It’s fire resistant.
2: Disadvantages:
It does not work for a 100% as insulation.

## Slide 25
Only applicable to facades in good condition
    Is expensive, but pays for itself
MEC DECOR WWW.Spuit-kurk.be